Running NIOSV through On-Chip-Ram (16-bits)

Aim : To run the NIOSV software code through On-Chip-Ram where the data width of the
        On-Chip-Ram IP is 16 bits.

Description : The requirement of the design is to build a hardware system having NIOSV processor which will be running through On-Chip-RAM IP with 16 bits configuration.
After following the below steps, somehow not able to execute the NIOSV code. Please refer the below snap shots of the hardware and software design.

Target Device : Cyclone IV E ( EP4CE40F23C8 )

Hardware Design :

BSP settings:

Generated the CmakeLists.txt file successfully after BSP generation. Created software project as well and was able to build the software project successfully.

Also the ELF was downloaded on the board successfully, but somehow the NIOSV code does not exectued.

Please refer the snap shot of Debugger console while running the ELF from On-Chip-Ram.

Debugging:

As NIOSV code was not executed, the ELF was run through “Ashling RISCV (auto-detect) Hardware Debugging” option. The NIOSV was stuck at the below point with a pop up error window.

Note: The above issue arises only when the On-Chip-RAM Data Width is set to 16 bits. The
        NIOSV code executes successfully if On-Chip-RAM Data Width is set to 32 bits.

Please share your feedback for to execute NIOSV code with 16 bit ON-CHIP-RAM!!